## Slide 1
GPU SPARSE COMPUTATION
ILU0 dependency scheduling benchmarks
Wavefront and sync-free execution on SuiteSparse bcsstk36
Row-dependency kernel study
Based on the repository's saved benchmark results

## Slide 2
SCOPE
What was measured?
Source: local ILU0 benchmark code and saved SuiteSparse bcsstk36 results
02
Each row waits for earlier rows
For every lower-triangular entry j < i, row i reads the result of row j. That gives a directed edge j → i in the dependency graph.
Benchmark loop
row_done[i] = 1 + Σ row_done[j] for j < i in row i
This is a dependency surrogate. It does not compute the numerical ILU0 factors.
The study isolates scheduling and DAG preparation costs.

## Slide 3
METHOD
One dependency graph, two schedulers
Source: local ILU0 benchmark code and saved SuiteSparse bcsstk36 results
03
Wavefront: synchronized batches
A B
C D
E
Launch a wave → wait for all rows → launch the next wave
Sync-free: ready rows proceed
A
B
C
D
E
One launch; atomic counters release each row when ready
‘Sync-free’ removes global wave barriers; rows still coordinate through atomic counters.

## Slide 4
BENCHMARK DESIGN
How to read the five methods
Source: local ILU0 benchmark code and saved SuiteSparse bcsstk36 results
04
GPU end to end
Build the DAG and schedule, prepare device arrays, execute on GPU, and copy the result back.
GPU prepared
DAG and device arguments are prepared before timing. Sync-free resets its counters on every measured run.
CPU
Execute the same row-dependency loop sequentially. No GPU setup or transfer is needed.
Prepared = steady-state execution; end to end = one run on a new sparsity pattern.

## Slide 5
RESULTS · LOWER IS BETTER
Measured latency on bcsstk36
Source: local ILU0 benchmark code and saved SuiteSparse bcsstk36 results
05
SuiteSparse matrix · 23,052 × 23,052 · 1,143,140 nonzeros
Wavefront E2E
521.9 ms
GPU
Wavefront Prepared
261.0 ms
GPU
Sync-free E2E
244.7 ms
GPU
Sync-free Prepared
28.6 ms
GPU
CPU
93.9 ms
CPU
Times reconstructed from saved rows/s; the benchmark reports the median.

## Slide 6
ONE-SHOT DECISION
For one new matrix pattern, CPU wins
Source: local ILU0 benchmark code and saved SuiteSparse bcsstk36 results
06
CPU
93.9 ms
Sync-free GPU E2E
244.7 ms
The GPU end-to-end path takes 2.6× as long.
DAG construction, allocation, transfer, and result copying are paid on every one-shot run.

## Slide 7
REPEATED PATTERN
Preparation can pay off when reused
Source: local ILU0 benchmark code and saved SuiteSparse bcsstk36 results
07
Approximate initial cost: 216.1 ms · prepared run: 28.6 ms
Repeated runs
1 run
CPU 94 ms
GPU 245 ms
2 runs
CPU 188 ms
GPU 273 ms
3 runs
CPU 282 ms
GPU 302 ms
4 runs
CPU 376 ms
GPU 330 ms
10 runs
CPU 939 ms
GPU 502 ms
Illustrative break-even: ~4 runs with the same sparsity pattern. This estimate subtracts separate benchmark measurements; measure a true repeated-run workflow next.

## Slide 8
TAKEAWAYS
What the benchmark supports
Source: local ILU0 benchmark code and saved SuiteSparse bcsstk36 results
08
1 · Scheduler matters
Prepared sync-free is 9.1× faster than prepared wavefront on bcsstk36.
2 · Setup matters
The CPU wins a one-shot run. Reusing the same sparsity pattern can amortize preparation.
3 · Next experiment
Benchmark numerical ILU0 itself, measure the preparation stages separately, and test more real matrices.
Claim this as a row-dependency scheduling result, not a full ILU0 speedup.